NOTES TO SPECIFIER:  Items in BLUE font are edit prompts and notes that should be deleted from final section.

- Specifications are for electronic access control locksets, exit device trim and handheld programming devices and as such, are only part of a complete access control installation.  Copy and paste information into complete specification section as required.

- Text in GRAY FONT is provided for reference and in locating applicable articles within the specification.

- Typical edit prompts: Explanation

EDIT/NOTE = Flag with instructions to the specifier on options/selections.

[Brackets] = Options.  Delete brackets and turn off bold to include.

<Carrots> = Text Insert.  Turn off bold, replace text and delete carrots.

NAVIGATION SHORTCUTS:  Hover the cursor over bold, underlined text and follow instructions for shortcut link to specified item.

CO-100-CY: Bored, Cylindrical-Type EAC Lockset

CO-100-MS/MD: Mortise-Type EAC Lockset

CO-100-993: Exit Device Trim EAC Lockset

SCHLAGE CO-100
ELECTRONIC ACCESS CONTROL LOCKSET

GENERAL

NO INFORMATION INCLUDED IN PART 1 OF THIS TEMPLATE

products

materials

Fasteners: Manufacturer’s standard corrosion-resistant, nonstaining, nonbleeding fasteners and accessories compatible with adjacent materials.

electronic access control locksETS – STANDALONE bored-type Proprietary – co-100-cy

Manufacturer: “CO-100-CY” series, as manufactured by Schlage Company. No substitutes will be accepted.

Requirements: Standalone electronic locksets shall comply with the following requirements.

Type: Heavy-duty, bored cylindrical, non-handed, field-reversible.

Backset: 2-3/4-inch (70 mm) standard, with 2-3/8-inch (60 mm), 3-3/4-inch (95 mm) and 5-inch (127 mm) backset optional.

Latchbolt Throw: 1/2-inch (13 mm) with optional 3/4-inch (19 mm) throw available.

Chassis: Shall accommodate standard 161 cylindrical lock prep for 1-3/4-inch (44 mm) doors standard, or 1-3/8-inch (35 mm) to 2-3/4-inch (70 mm) thick doors in 1/8-inch (3 mm) increments.

Applicable Standards:

Listed, UL 294 - The Standard of Safety for Access Control System Units.

Compliant with ANSI Standard A156.25 and A156.2 Series 4000, Grade 1 strength and operational requirements.

Compliant with ANSI/BHMA A156.25 Grade 1 Operation and Security Requirement.

Certified to UL10C, FCC Part15, Florida Building Code Standards TAS 201 large missile impact, TAS 202 and TAS 203.

Compliant with ASTM E330 for door assemblies.

Compliant with ICC / ANSI A117.1, NFPA 101, NFPA 80, and Industry Canada RSS-210.

Lockset Functions: Provide locks with following functions, as scheduled, that are field configurable without taking the lock off the door:

EDIT – as required

Classroom / Storeroom 70.

Office 50.

Emergency Override: Lockset shall have the ability to utilize emergency mechanical key override with multiple manufacturer’s key systems in the lever including:

Full Size cylinders from Schlage and Sargent up to 6-pin cylinders and Falcon up to 7-pin cylinders.

Full Size Interchangeable Cores from Schlage, Sargent, Corbin Russwin, Medeco, and Yale format by Medeco in up to 6 pin cylinders

Small Format Interchangeable core up to 7 pin by Schlage, Falcon, BEST, Sargent, Corbin Russwin, Medeco, Yale, and others.

Levers:

Vandal Resistance: Exterior (secure side) lever designed with ability to rotate freely while door remains securely locked, preventing damage to internal lock components from vandalism by excessive force.

Lever trim to be non-handed, and to operate independently of non-locking levers for extended life cycles.

Style: Sparta[Rhodes][Athens][Tubular]

Tactile Warning (Knurling): Provide on levers on exterior (secure side) of doors serving rooms considered to be hazardous by the authority having jurisdiction.

Power Supply:

Lockset powered by four AA batteries.

Lockset shall have ability to communicate battery status.

Features:  Locksets shall incorporate the following features.

Visual tri-colored LED indicators that indicate activation, additional PIN code credential required, operational systems status, system error conditions and low power conditions.

Audible feedback that can be enabled or disabled.

Onboard processor with memory capacity of 500 users.

Tamper-Resistant Screws: Tamper torx screws on inside escutcheon for increased security.

Credential Reader Capabilities:  Integrated 12 button, backlit keypad.

electronic access control locksETS – STANDALONE Mortise-type Proprietary – co-100-ms

Manufacturer: “CO-100-MS” series, as manufactured by Schlage, an Ingersoll Rand Company. No substitutes will be accepted.

Requirements: Standalone electronic locksets to comply with the following requirements.

Type: Mortise, field-reversible handing.

Backset: 2-3/4-inch (70 mm), nominal.

Latchbolt: 3-piece, beveled, stainless steel with 3/4-inch (19 mm) throw and anti-friction latch.

Chassis: Shall accommodate ANSI standard mortise lock prep for 1-3/4-inch (44 mm) doors standard, or 1-3/8-inch (35 mm) to 2-3/4-inch (70 mm) thick doors in 1/8-inch (3 mm) increments.

Applicable Standards:

Listed, UL 294 - The Standard of Safety for Access Control System Units.

Compliant with A156.25 and A156.13 Series 1000, Grade 1 Operational and Security.

Certified to UL10C, FCC Part15, Florida Building Code Standards TAS 201 large missile impact, TAS 202 and TAS 203.

Compliant with ASTM E330 for door assemblies.

Compliant with ICC / ANSI A117.1, NFPA 101, NFPA 80, and Industry Canada RSS-210.

Lockset Functions: Provide locks with following functions, as scheduled, that are field configurable without taking the lock off the door:

EDIT – as required

Classroom / Storeroom 70.

Office 50.

Emergency Override: Lockset shall have the ability to utilize emergency mechanical key override with multiple manufacturer’s key systems in the lever including:

EDIT – as required for cylinders/cores

Full Size cylinders from Schlage and Sargent up to 6-pin cylinders and Falcon up to 7-pin cylinders.

Full Size Interchangeable Cores from Schlage, Sargent, Corbin Russwin, Medeco, and Yale format by Medeco in up to 6 pin cylinders

Small Format Interchangeable core up to 7 pin by Schlage, Falcon, BEST, Sargent, Corbin Russwin, Medeco, Yale, and others.

Levers:

Vandal Resistance: Exterior (secure side) lever designed with ability to rotate freely while door remains securely locked, preventing damage to internal lock components from vandalism by excessive force.

Operation: Outside and inside levers operate independently of each other.

Style: Sparta (17)[Rhodes (06)][Athens (07)][Tubular (03)]

Tactile Warning (Knurling): Provide on levers on exterior (secure side) of doors serving rooms considered to be hazardous by the authority having jurisdiction.

Power Supply:

Lockset powered by four AA batteries.

Lockset shall have ability to communicate battery status.

Features:  Locksets shall incorporate the following features.

Visual tri-colored LED indicators that indicate activation, additional PIN code credential required, operational systems status, system error conditions and low power conditions.

Audible feedback that can be enabled or disabled.

Onboard processor with memory capacity of 500 users.

Tamper-Resistant Screws: Tamper torx screws on inside escutcheon for increased security.

Credential Reader Capabilities:  Integrated 12 button, backlit keypad.

ELECTRONIC ACCESS CONTROL – STANDALONE EXIT DEVICE TRIM Proprietary – CO-100-993

Manufacturer: “CO-100-993” series, as manufactured by Schlage, an Ingersoll Rand Company. No substitutes will be accepted.

Requirements: Standalone electronic exit device trim shall comply with the following requirements.

Type: Exit device trim, non-handed, field-reversible.

Exit Device Configurations: Exit device lever trim to retract latchbolt for the following exit device applications:

Rim

NOTE – The following are applicable to Von Duprin 98/99/22 only.

Surface vertical rod

NOTE – The following are applicable to Von Duprin 98/99 only.

Mortise

Concealed vertical rod

Exit Device Compatibility: Provide exit device trim with universal mounting plate enabling operation as follows:

EDIT – as required for configurations and manufacturer series.

All Von Duprin 98/99 Series exit device configurations.

Von Duprin 22 Series rim and surface vertical rod configurations.

Rim exit devices from [Falcon 25 Series][, Sargent 80 Series][, Corbin-Russwin 5000 Series][, Dorma 9300 Series][, Precision 21 Series][, Yale 7000 Series]NOTE: Precision 2100 converts to 21 w/ Precision BP21 kit.

Applicable Standards:

Listed, UL 294 - The Standard of Safety for Access Control System Units.

Compliant with ANSI/BHMA A156.25 Grade 1 Operation and Security Requirement.

Certified to UL10C, FCC Part15, Florida Building Code Standards TAS 201 large missile impact, TAS 202 and TAS 203.

Compliant with ASTM E330 for door assemblies.

Compliant with ICC / ANSI A117.1, NFPA 101, NFPA 80, and Industry Canada RSS-210.

Exit Device Trim Functions: Provide locks with following functions, as scheduled, that are field configurable without taking the lock off the door:

Classroom / Storeroom.

Emergency Override: Exit device trim shall have the ability to utilize emergency mechanical key override with multiple manufacturer’s key systems in the lever including:

EDIT – as required for cylinders/cores

Full Size cylinders from Schlage and Sargent up to 6-pin cylinders and Falcon up to 7-pin cylinders.

Full Size Interchangeable Cores from Schlage, Sargent, Corbin Russwin, Medeco, and Yale format by Medeco in up to 6 pin cylinders

Small Format Interchangeable core up to 7 pin by Schlage, Falcon, BEST, Sargent, Corbin Russwin, Medeco, Yale, and others.

Levers:

Vandal Resistance: Exterior (secure side) lever designed with ability to rotate freely while door remains securely locked, preventing damage to internal lock components from vandalism by excessive force.

Style: Sparta (17)[Rhodes (06)][Athens (07)][Tubular (03)]

Tactile Warning (Knurling): Provide on levers on exterior (secure side) of doors serving rooms considered to be hazardous by the authority having jurisdiction.

Power Supply:

Exit device trim powered by four AA batteries.

Exit device trim shall have ability to communicate battery status.

Features:  Exit device trim shall incorporate the following features.

Visual tri-colored LED indicators that indicate activation, additional PIN code credential required, operational systems status, system error conditions and low power conditions.

Audible feedback that can be enabled or disabled.

Onboard processor with memory capacity of 500 users.

Tamper-Resistant Screws: Tamper torx screws on inside escutcheon for increased security.

Credential Reader Capabilities: Integrated 12 button, backlit keypad.

FINISHES

Electronic Access Control Locksets[ and Exit Device Trim]: Provide metal finish complying with BHMA A156.18, as indicated below[ and where indicated in door hardware sets].

EDIT – Select one, or if multiple required, defer to door hardware schedule edit option above.

605 (Bright Brass)

606 (Satin Brass)

612 (Satin Bronze)

643e (Aged Bronze)

619 (Satin Nickel)

625 (Bright Chrome)

626 (Satin Chrome)

626AM (Satin Chrome, Antimicrobial)

EXECUTION

NO INFORMATION INCLUDED IN PART 3 OF THIS TEMPLATE

END OF SECTION